## Slide 1: Laser Light Show
ELEC 391 – Group B1 ( Control )

## Slide 2: Simulink Model

## Slide 3: RCGs
Requirements
PID Values Obtained
Encoder Detects Position and Direction
Constraints
Max Memory / Speed of Microcontroller
Max Motor Current ( < 1A )
Goals
Rise Time ( < 0.017 s )
Overshoot ( < 10 % )
Functioning Microcontroller
No Breadboards
Max Encoder Resolution ( 400 pulses )
Simulink Model of Motor Within 5 % Error

## Slide 4: The Process
Find Motor Parameters
Encoder PCB
System Setup
Controller Code

## Slide 5: Motor Parameters
R, L (8.4 , 1.12mH)
R, L (8.4 Ω , 1.12mH)
Measured using multimeter
( 23.54 )
Kτ ( 23.54 mNm/A )
J ( )
J ( 5.93×〖10〗^(−6) kg m^2 )
B ( 4.964 )
B ( 4.964 ×〖10〗^(−6) (kg m^2)/s )
Torque determined from conservation of power
Calculated from mechanical time constant
Kv ( 628.5 )
Kv ( 628.5 RPM/V )
Back EMF calculated from KVL
Kinetic friction from at no load conditions
Kinetic friction from 𝑡𝑜𝑟𝑞𝑢𝑒/𝑓𝑟𝑖𝑐𝑡𝑖𝑜𝑛 at no load conditions
Resistance and Impedance
Torque Constant
Rotor Inertia
Back EMF
Kinetic Friction

## Slide 6: Checking Motor Parameters
Chart: Directly Driving Motor

## Slide 7: Closed Loop Simulink Model
Maps PWM to Average Voltage
Quantizes Angle to Encoder Resolution
PWM Value between
0 - 255
Motor Transfer Function
Rounds PWM to Integer
Model Behaviour for Low PWM Values

## Slide 8: Controller Logic – Reading Position
State 01
State 11
State 00
State 10
Increment
Decrement
State
<A> <B>
On Encoder A Interrupt
A ^ B
Read Encoder A
Position++
Position--
End
On Encoder B Interrupt
A ^ B
Read Encoder B
Position++
Position--
End

## Slide 9: Initial Control
12.43 | 11.1 | 1.1 | 12783.9
12.43 | 11.1 | 1.1 | 12783.9
Aim for fastest rise time and smallest overshoot
Ensure system is stable
Overshoot | 
Rise Time | 
Settle Time | 
Control Frequency | 

## Slide 10: Controller Logic – PID Control
Proportional
Subtract current position from desired position for error value
Multiply by proportional gain
Integral
Keep sum of error values at small intervals
Multiply by integral gain
Derivative
Save position value every millisecond for velocity
Multiply velocity by derivative gain (negative)
Reset sum for each new coordinate

## Slide 11: P Control
Modified MATLAB Model accounts for values of PWM less than 30 being too low to overcome cogging and static friction

## Slide 12: PD Control
Simulink model adjusted for derivative control on current velocity instead of rate of error change.
This results in a negative derivative gain.

## Slide 13: Performance
Overshoot | ~ 5 %
Rise Time | ~ 0.13 s
Settle Time | ~ 0.3 s
Control Frequency | ??
Chart: 

## Slide 14
SYSTEM
INSERT IMAGE OF CAD MODEL FOR SYSTEM

## Slide 15: System PCB
Pins from Encoder
Extra 5V Pins
Diode Bridge
Arduino Base
Current Driver
12V Input Pins

## Slide 16: Homing
dfsa

## Slide 17: Mapping
Map desired laser path to list of coordinates
Inverse kinematics are applied to obtain angles
Angles are converted to encoder positions
Time vector is generated based on length of each line segment
0.8, -0.2
-0.7, 0.6
0.8, -0.2
-0.7, 0.6
= 7 pulses
Points:
< n pulses >
Time:
< relative length>
To Controller
1
2
3
4

## Slide 18: Next Steps - Integration
Measure new motor parameters
Adjust system integration design
Improve gear ratios
Retune PIDs

## Slide 19: Garbage Slide